## Slide 1: PID Controller Design and Tuning
Presented by Joe Driscoll and Isaac Hill

## Slide 2: Problem and Requirements
Design a motor controller
  Basic requirements
    5% steady state error
    < 10% overshoot
    Closed loop response 50% faster than open loop

## Slide 3: Solution
Use PID controller:
  Adjustable/adaptable
  Quick response time
Design focused heavily on response time
https://commons.wikimedia.org/wiki/File:Change_with_Ki.png
Notes: Proportional, integral, derivative
The graph on the right shows how the controller can be changed with different values. This graph shows different values for only one of the variables.
More adjustable – multiple variables allows different ways to sense error, a lot of control over the response

## Slide 4: PID Controller
The PID controller transfer function:
https://nicisdigital.wordpress.com/2011/06/27/proportional-integral-derivative-pid-controller/
PID controller design:
  proportional gain (Kp) – error sensitivity
  integral gain (Ki) – steady state error
  derivative gain (Kd) – stability and speed
Notes: The proportional gain is what causes the controller to respond to different levels of error.
The integral gain lets the controller react to past error values. This eliminates any persistent error that the proportional gain does not correct.
The derivative gain estimates the future error. This constant helps eliminate any error at a faster pace.
Kp and Ki decrease rise time, but increase overshoot
Ki significantly decreases steady state error,
Kd improves stability and has minor effect on other variables
Proportional gain – sensitivity to error
Integral gain – reduces steady state error
Derivative gain – improves settling time and stability
S-domain = frequency domain
e(t) is error function.
We’ll actually use a discrete time domain, because computers are only capable of sampling

## Slide 5: Discrete PID Equations
PID equation
  , functions of , , , and T
  3 adds and 3 multiplies for one control step
Gains can be changed at run-time
  Possible to manually tune
  Code provides special mode for tuning
Notes: Uses an array
Tuning

## Slide 6: Tuning Approaches
Methods attempted/used
  Cohen-Coon (most difficult)
  Ziegler-Nichols
  Manual tuning (least difficult)
Floating point unit difficulties
  PID gains tend to be low
Used manual tuning rather than adapting system for small gains

## Slide 7: Ziegler-Nichols
Simple gain equations/process
  Find ultimate gain and period ( )
Values from testing
  under 20
  under 1
  Still issues with floating point

## Slide 8: Cohen-Coon
Gain calculations
  Parameters calculated from previous lab
Resulting gains still too low
http://blog.opticontrols.com/archives/316

## Slide 9: Tuning Results
Tuning resulted in PI controller
  -
  -
  -
Unexpectedly large gains
  Proportion determined performance (not scale)
Controller only makes two control actions (0% or 100% duty cycle)
  Effectively schedules pulses
  Rise time > fall time transient

## Slide 10: Open Loop Captured Data
622 ms

## Slide 11: Closed Loop Captured Data
280.2 ms

## Slide 12: Closed Loop Response Summary
Same transition from 480 mV to 900 mV
~50% faster settling time
  Open loop: 620-640 ms
  Closed loop: 280-300 ms
Minimal ripple (under 10 mV)
Possible improvements:
  Scale up errors
  Use MCU with FPU
  Optimize error calculations/tuning interface

## Slide 13: Questions?